In Device State 2 q1 and q0 are don’t cares. Data conversion as per Signal Source two bit packed shown in Table 1.
Table 1: Device State 2 Raw Data
Byte 1
t0				t1 (t0 + 61 ns)
Bit7 (msb)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
q1	q0	i1	i0	q1	q0	i1	i0
Byte 2
t2 (t0 + 122 ns)				t3 (t0 + 183 ns)
Bit 7 (msb)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
q1	q0	i1	i0	q1	q0	i1	i0

The data conversion for this type of raw file entails splitting each byte into two bytes using a bit wise ‘and’ to extract the bits of concern. The first bit wise and is with a 0x30 followed by a right shift of 4 bits. The second bit wise and is with 0x03 and no bit shift. The result is samples separated into their own byte as show in Table 2.
Table 2: Device State 2 Raw Data Separated Before Conversion
Byte 1
t0
Bit7 (msb)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
x	x	x	x	x	x	i1	i0
Byte 2
t1 (t0 + 61 ns)
Bit7 (msb)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
x	x	x	x	x	x	i1	i0
Byte 3
t2 (t0 + 122 ns)
Bit7 (msb)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
x	x	x	x	x	x	i1	i0
Byte 4
t3 (t0 + 183 ns)
Bit7 (msb)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
x	x	x	x	x	x	i1	i0

The raw values are then translated into signed integers and written to a binary data file. The converted data should end up looking like Table 3.
Table 3: Device State 2 Converted Data
Byte 1
t0
Bit7 (sign)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
1|0	0	0	0	0	0	1|0	1|0
Byte 2
t1 (t0 + 61 ns)
Bit7 (sign)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
1|0	0	0	0	0	0	1|0	1|0
Byte 3
t2 (t0 + 122 ns)
Bit7 (sign)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
1|0	0	0	0	0	0	1|0	1|0
Byte 4
t3 (t0 + 183 ns)
Bit7 (sign)	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0 (lsb)
1|0	0	0	0	0	0	1|0	1|0